Model 11 - Static Electricity

Worksheet 3 - Calculating Electric Field, Potential & Energy

- Use Coulomb’s Law and the definition of Electric Field to derive an equation for the electric field around a point charge.

- What is the relationship between the electric field strength and the distance from the point source? If you move three times farther away, what will happen to the field strength?

- What is the relationship between the electric field strength and the charge of the point source? If the charge of the point source is increased by a factor of three, what happens to the electric field strength?

- What is the magnitude and direction of the electric field 0.25 meters away from a point charge with - 5.0 C. Use proportional reasoning to find the field strength at positions 0.125 meters away and 0.75 meters away.

- Consider a fixed charge of +2 μC. What is the magnitude of the electric field at a distance of 10 cm away from the charge?

- The plates of a parallel plate capacitor have a uniform charge of +1.0 C and -1.0 C, respectively. If the uniform electric field between the plates is 6200 N/C and they are connected across a potential difference of 1500 V, what is the distance between the plates?

- How much is the electrical potential is between two evenly electrified parallel flat plates, distanced d = 8 cm, if the strength of electric field between them is E = 75 N/C?

- Two oppositely charged parallel plates are separated by a distance of 0.2 m. The uniform electric field between them has a magnitude of 1800 N/C.

  - What is the electric potential between the plates?

  - How must work is required to move an electron 0.15 m between the plates? (Hint: go back to what you learned about work in the energy model)