Name

Unbalanced Force Model:

Homework

1. An 80 kg water skier is being pulled by a boat with a force of 220 N causing the skier to accelerate at 1.8 m/s2. Find the drag force on the skier.

2. A 2000 kg car is slowed down uniformly from 20 m/s to 5 m/s in 4 seconds. Determine the average net force on the car during this time, and how far the car traveled while slowing down.

3. Some baseball pitchers are capable of throwing a fast ball at 100 mi/hr. The pitcher achieves this speed by moving his arm through a distance of 1.5 m. Determine the average net force that must be exerted on the 0.15 kg ball during the pitch. (1 mile = 1600 meters)

4. After falling from rest at a height of 30 m, a 0.50 kg ball bounces upward, reaching a height of 20 m. The contact between the ball and ground lasted 2 milliseconds. Find the average force exerted on the ball by the ground. (Break the problem into pieces. Do a bunch of kinematics first, then apply Newton’s 2nd law.)

5.

The cord is 25˚ above the horizontal.

mass of kids and sled = 100 kg

Tension in cord is 120 N.

Friction force is 15 N.

Find the acceleration of the sled.

6.

The hill is at a 35˚ angle.

skier’s mass is 60 kg.

coefficient of friction is 0.08

Determine the acceleration of the skier.